Hand tool, machines and systems for final packaging and transport securing.

Technical data OR-T 250

| Weight incl. battery | 3.9 kg (8.6 lbs) |
| --- | --- |
| Strap width, adjustable | 12-13、15-16 mm |
| Strap thickness | 0.5–1.0mm (.020–.039") |
| Tension Power | 90－250kg (900－2500N) |
| Strapping with one battery charge | up to 400 cycles |
| Power supply battery | 14.4V, 2.6Ah, Bosch |
| Option | Suspension bow Protection plate Protection cover Power supply |