OR-T 250/400

A QUANTUM LEAP

IN STRAPPING

Easy

Fast

Safe

Economic

Environmentally-friendly

Patented

OR-T 250/400

Quantum leap:

Strapping with only one push of a button!

Easy

Technical data	OR-T 250	OR-T 400

Universal applications	•

Heavy applications	•

Weight (incl. battery), kg	3.9 	4.2 	Dimensions

–Length, mm	334	334	–Width, mm	138	138	–Height, mm	148	148	Tensioning force, N	(0) 900–2500	(0) 1200–4000 	–Soft, N	(0) 400–1500	(0) 400–1600 	Tensioning speed, mm/s	220	175 	Friction-weld-seal	•	•	Battery charger, battery

Charger voltage, V	100, 110, 230	100, 110, 230 	Battery charging time, min.	15–30*	15–30*	No of cycles per battery,

up to	200–400**	180–300**	Battery: Li-Ion (Bosch)	14,4 V, 2.6 Ah	18 V, 2.6 Ah	Plastic strap

Polypropylene (PP)	•	•	Polyester (PET)	•	•	Width, mm	12–13, 15–16	16–19 	–Option, mm	  9–11

Thickness, mm	0.5–1.0 	0.8–1.3

Options

–Suspension bow	•	•

–Protection plate	•	•

–Protection cover	•	•

–Power supply	•	•

* After 15 minutes, approx 70% charge capacity

** Depending on strap quality, tension and package

•	Depending on application,

adjustable operation

mode

•Fully automatic

•Semi-automatic

•Manual

•Soft

Safe

Environmentally-friendly

Fast

Latest brushless motor

engineering with the latest environmental-friendly

battery technology from Bosch:

•	High efficiency ratio

•	No memory effect

•	Recharging at any time

•	High number of strappings

Regardless of package, size, vertical or horizontal strapping:

•Fully or semi-automatic

tensioning, welding, and

strap cutting – with only

one push of a button

For multiple strapping or

for the same types of goods:

•Consistent strappings

•Automatic strapping

eliminates operator error

Strapping with PP strap or

for fragile packages:

•“Soft“ mode

08.2014Subject to modification

Economic

•Energy-efficient

strapping system

•More cycles per battery

charge

•Cost efficient

•Service-friendly

construction

•High quality

Developed and

manufactured

in Switzerland

ORGAPACK GmbH

Packaging Technology

Silbernstrasse 14

CH-8953 Dietikon

Phone	+41 44 745 50 50

Fax	+41 44 745 52 16

pt@orgapack.com

www.orgapack.com

Certificate ISO 9001 / EN 29001

www.orgapack.com