P327  Battery powered manual plastic strapping tool

Characteristics

| Strapping qualities | Polypropylene(PP)and Polyester(PET) |
| --- | --- |
| Strapping dimensions widths | 16.0-19.0mm / 5/8-3/4” |
| Strapping dimensions thicknesses | 0.40-1.35mm / 0.016-0.053” |
| Weight incl. battery | 4.1kg / 9.0lbs |
| Tool sizes with battery | L350*W128*H130mm / 13.8”*5”*5.1” |
| Average seal strength | up to 75%(dependent on strap quality) |
| Type of seal | Friction weld sealing |
| Strep tension | 600-3500N / 135-790 lbs(adjustable) |
| Tensioning speed | 55-130mm/s / 2.2-5.1 inch/s |
| Power supply Battery | 18VDC / 3.0Ah Li-lon |