AP-16   Semi-Automatic Strapping Machine

FEATURES: Standard accessory, its advantage is stable quality, durable material, and easy maintenance. Special design-Control PP strap cooling time. It can make the PP strap to fasten well in any time. "Electricity-saving" device, the motor automatically stops running after 60 seconds pause to reduce the regular mechanical wear and to prolong the machine's life. The advanced P.C.B microchip circuit board control system, less malfunction and easy maintenance. Durable electro-magnetic clutch transmission means lesser mechanical wear and noise pollution. New heater plate design improves warm-up-time, weiding speed and increase work efficiency. Installing an auxiliary feed switch and cut switch at the control panel makes you operate more conveniently. Height can be adjusted. Each hole is 14 mm, one section. If locked 2 screws, can increase the height 70mm. If lock 1 screw, can increase the height 140mm. If the machine is with outside tension, then the model number is PW-616HS, PW-616LS, PW-616SLS . (For PW-616H only) Standard dispenser inside dia. is 200mm. If need dia. 230 or 280mm, the inner plates required. Legs and dispensers are disassembled to save transportation costs. 3 units packed in one pallet. 126 units loaded in a 20' feet container. SPECIFICATIONS: Model AP-16 AP-16L AP-16SL Power supply 1 Ø AC110,220V(50,60Hz), 1/4HP Strap width 6,9,12,15 mm (adjustable) Tension strength 15~50kgs Strapping speed 2.0 sec./strap Min. package size 60mm Max. package size Any size Dimension (LxWxH) (mm) 910x580x750 1460x580x480 1460x580x330 N.W. 100kgs 90kgs 80kgs G.W. 120kgs 110kgs 90kgs Packing size (LxWxH) (mm) 956x626x914 Machine: 956x626x992 Dispenser:956x626x595 Machine: 956x626x842 Dispenser:956x626x443 Note: Specifications subject to change without notice.