OR-T 120

STRAPPING

MADE EASY

Easy

Fast

Ergonomic

Economic

Environmentally-friendly

Patented

Strapping made easy:

Strapping with only one push of a button!

OR-T 120

Easy

Technical data	OR-T 120

Light applications	•

Weight (incl. battery), kg	3,4

Dimensions

–Length, mm	320

–Width, mm	138

–Height, mm	148

Tensioning force, N	(0) 400–1200

–Soft, N	(0) 150–750

Tensioning speed, mm/s	220

Friction-weld seal	•

Battery charger, battery

Charger supply voltage, V	100, 110, 230	Battery charging time, minutes	20–45*

No of cycles per battery,

up to	200–300**

Battery: Li-Ion (Bosch)	14,4 V, 1,3Ah

Plastic strap

Polypropylene (PP)	•

Polyester (PET)	•

Width, mm	9/11–13

Thickness, mm	0,35–0,85

Options

–Suspension bow	•

–Protection plate	•

–Protection cover	•

* After 20 minutes, approx 75% charge capacity

** Depending on strap quality, tension and package

Selectable mode to suit application:

•Fully automatic

•Semi-automatic

•Manual

•Soft tension

Ergonomic

Environmentally-friendly

Fast

11.2012Subject to modification

Latest brushless motor with the latest Li-Ion environmentally friendly battery technology from Bosch:

•	High efficiency motor

•	No memory effect

•	Recharging at any time

•	High number of cycles

Regardless of package, size, vertical or horizontal strapping:

•Fully or semi-automatic

tensioning, welding, and

strap cutting – with only

one push of a button

•Very light weight: 3,4 kg

•Automatic welding

function, no keystroke

needed

•Consistent strapping

•Automatic strapping

reduces operator error

Economic

•Energy-efficient

strapping system

•More cycles per battery

charge

•Cost efficient

•Service-friendly

construction

•High quality

Developed and

manufactured

in Switzerland

ORGAPACK GmbH

Packaging Technology

Silbernstrasse 14

CH-8953 Dietikon

Phone	+41 44 745 50 50

Fax	+41 44 745 52 16

pt@orgapack.com

www.orgapack.com

Certificate ISO 9001 / EN 29001

www.orgapack.com