Datasheet P326

Battery powered manual plastic strapping tool

Battery powered plastic strapping tools

Characteristics

Stapping dimensions: widths 10.0 – 16.0 mm / 3/8 – 5/8�

Tool sizes with battery: L350 x W122 x H130 mm / 13.8� x 4.8� x 5.1�

Type of seal: 	Friction weld sealing

Tensioning speed: 	85 – 190 mm/s / 3.3 – 7.5 inch/s

Suspension bracket (optional)

Advantages

Complies with the European Safety Regulations EN 415-8

New reinforced 18V motor

Li-Ion battery technology

Very high capacity of up to 600 strap cycles per battery load (dependent on strap quality and dimension)

Battery protection

Simple one-handed operation

Very high tension force with adjustable tension speed

Tension force and sealing time adjustable

FROMM Holding AG

Tel. +41 (041) 741 57 41

Datasheet P326

Battery powered manual plastic strapping tool

Chart of types model P326

Item No. Model Strap widths Strap thicknesses Max. Tension Tension speed

43.2202 P326/10/0.65-1.05 10.0 3/8� 0.65-1.05 .026-.041 2400 540 85-190 3.3-7.5

43.2212 P326/11.1/0.65-1.05 11.1 7/16� 0.65-1.05 .026-.041 2400 540 85-190 3.3-7.5

43.2222 P326/12/0.65-1.05 12 0.65-1.05 .026-.041 2400 540 85-190 3.3-7.5

43.2224 P326/12.7/0.65-1.05 12.7 �� 0.65-1.05 .026-.041 2400 540 85-190 3.3-7.5

43.2232 P326/13/0.65-1.05 13 0.65-1.05 .026-.041 2400 540 85-190 3.3-7.5

43.2252 P326/15/0.65-1.05 15 0.65-1.05 .026-.041 2400 540 85-190 3.3-7.5

43.2254 P326/15.5/0.65-1.05 15.5 0.65-1.05 .026-.041 2400 540 85-190 3.3-7.5

43.2262 P326/16/0.65-1.05 16 5/8� 0.65-1.05 .026-.041 2400 540 85-190 3.3-7.5

Battery chargers for model P326

| Item No. | Model | Tension | Power |
| --- | --- | --- | --- |
| N5.4330 | Accu Li-Ion | 18VDC | 3.0 Ah |
| Accessories |  |  |

| Item No. | Model | Tension | Power |
| --- | --- | --- | --- |
| N5.4330 | Accu Li-Ion | 18VDC | 3.0 Ah |
| Accessories |  |  |

P32.0112 Standard suspension bracket P32.0137 Suspension bracket for alternating positions

FROMM Holding AG Tel. +41 (041) 741 57 41

Hinterbergstrasse 26 Fax +41 (041) 741 57 60

CH-6330 Cham www.fromm-pack.com

Switzerland hold.ch@fromm-pack.com