Datasheet A452

Pneumatic pusher type steel strapping tool

Pneumatic pusher type tensioner for round objects

Characteristics

| Strapping qualities: | Uniflex and Ultraflex max. 1100 N/mm2 / 160’000 psi |
| --- | --- |
| Strapping dimensions: widths | 19.0 – 32.0 mm / 3/4 – 1 1/4” |
| thicknesses | 0.63 – 1.27 mm / .025 - .050” |
| Weight: | 4.35 kg / 9.6 lbs |
| Strap tension: | 8500 N / 1900 lbs (6 bar / 87 psi) |
| Seals: | Overlap seals |
| Sealing: | With separate sealer model A412 or A461 |
| Suspension: | Eye bolt for standard applications is supplied with the tool |

Advantages

Very high strap tension up to 8500 N / 1900 lbs

After tensioning, the tool stops to tension, but no strap tension ever is lost (free wheeling system)

For safety reasons, the strap tension can be released at any time by pressing the black safety push button

The rugged tool permits a high strap tension and is particularly suitable for applications in the steel- and steel processing industries

The tension speed is very high Very silent operation of the tool

The light tool is ideal for non stationary applications

| FROMM Holding AG | Tel. +41 (041) 741 57 41 |
| --- | --- |
| Hinterbergstrasse 26 | Fax +41 (041) 741 57 60 |
| CH-6330 Cham | www.fromm-pack.com |
| Switzerland | hold.ch@fromm-pack.com |

Datasheet A452

Pneumatic pusher type steel strapping tool

Chart of types model A452

|  | Item No. |  | Model | Uniflex and Ultraflex |  | Max. Tension |  | Tension speed |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | max. 1100 N/mm2 / 160'000 psi |  |  |  |  |
|  |  |  |  | Width | Thicknesses |  |  |  |  |  |  |
|  |  |  |  | mm | inch | mm | inch | N | lbs |  | mm/s. | inch/s. |  |
|  | 13.4210 |  | A452/19-32/0.63-1.27 | 19-32 | ¾ - 1 ¼“ | 0.63 – 1.27 | .025-.050 | 8500 | 1900 |  | 150 | 5.9 |  |

| FROMM Holding AG | Tel. +41 (041) 741 57 41 |
| --- | --- |
| Hinterbergstrasse 26 | Fax +41 (041) 741 57 60 |
| CH-6330 Cham | www.fromm-pack.com |
| Switzerland | hold.ch@fromm-pack.com |